1. Interface definition
VDD	Driver power supply (+20~30V)	Input
VSS	Drive power ground	Input	power supply
MOT+	Motor drive positive signal	Output
MOT-	Motor drive negative signal	Output	Motor
CAN_H	CAN signal line	Two way
CAN_L	CAN signal line	Two way	CAN2.0B
LEFT	Left limit input signal	Input
RIGHT	Right limit input signal	Input
EN	External enable control (active high)	Input
FAULT	Fault output (collector open)	Output
GND	Control signal ground	Input	control signal
+5Vout	Encoder positive power supply	Output
A+	Encoder signal A channel +	Input
B+	Encoder signal B channel +	Input
Z+	Encoder signal Z channel +	Input
GND	Encoder power ground	Output	Encoder

2. Wiring diagram

3. Interface Description
(1) CAN_H / CAN_L: CAN2.0B signal, realize speed, position control, parameter setting, operation status monitoring, etc.;
(2) The EN signal is external enable control and is valid in any mode. When EN is high, the drive loads the motor . When EN at low level, the drive releases the motor and the motor is in a torque-free state. This signal is high when floating, when the driver load the motor.
(3) FAULT is the error signal that the driver outputs to the outside. The collector is open, and the user can pull up to 30V. When the system protection is generated, the output is low; in the normal state, the output is high. The input current is less than 5mA.
(4) LEFT is the left limit signal of the driver. When the signal changes from high level to low level, the left limit function will be triggered. at this time The drive will quickly control the motor to stop and remain enabled, at which point the drive control motor can only be to the right (clockwise)
Rotate, left will be blocked.
(5) RIGHT is the drive right limit signal. When the signal changes from high level to low level, the right limit function will be triggered. This When the drive will quickly control the motor to stop running and remain enabled, then the drive control motor can only be left (counterclockwise)
Rotate, the right will be blocked.
4. Installation size (unit: mm)
4. Software agreement
1. CAN communication
(1) Adopt CAN2.0B standard frame communication protocol, communication rate: 1000kbps, 500kbps, 250kbps, 125kbps, 100kbps, 50kbps, 20kbps can be set. 500kbps is the default communication rate setting.
Note : After modifying the communication speed of the drive, the host computer should also be modified to the same communication rate!
(2) Drive address ID code definition:
The master address ID code is 1, the drive address ID code range is 2~127, the ID code 0 is defined as the group call code, and the master can only pass the group call code.
All drives are controlled, but cannot be read back, ie the read command is invalid; where ID code 127 is the default factory setting of the drive.
2. Instruction structure
The driver communicates with the host computer using the CAN2.0B standard frame communication protocol . The servo control management system software provided by the company can
Dynamic graphics are generated to monitor the health of the motor in real time.
The composition of the instruction code: [Device ID] + [Instruction] + [Data]
[Device ID]: 1 byte, range 0~127;
[instruction]: 1 byte, range 0~255;
[Data]: None, 2 bytes or 4 bytes; 2 bytes make up 16-bit data, low byte first; 4 bytes make 32 digits according to the low byte first;
Note: To facilitate the description of the driver's instruction protocol, each hexadecimal instruction corresponds to an ASCII code instruction.
The "Servo Control Management System" software is operated by ASCII code instructions, and the system converts the ASCII code fingers into 16
After the command protocol is established, it communicates with the drive.
3. Instruction classification and address list
Instruction classification
Instruction classification subclass
Used address range
Reserved address range
Read drive product information command
0x01~0x02
0x03~0x0F
Motor encoder related configuration instructions
0x10~0x1F
0x20~0x27
Drive operating mode and node address setting command
0x28~0x2B
0x2C~0x2F
Drive operating parameter setting command
0x30~0x3E
0x3F~0x57
PID debug setting instruction
0x58~0x69
0x6A~0x74
Drive parameter settings
Instruction for storage
Into the EEPROM
Set boot to find zero command
0x75~0x7A
0x7B~0x7F
Drive system operation instruction
0x80~0x85
0x86~0x8F
Speed ​​control command
0x90~0x93
0x94~0x97
Position control instruction
0x98~0xA1
0xA2~0xAF
Drive control
Order, used to control the drive
Actuator operation
Other control modes (reserved)
no
0xB0~0xCF
Condition monitoring instruction
0xD0~0xD3
0xD4~0xDF
Production test instruction
Reserved
0xE0~0xFF

4. Parameter setting instruction for storage in EEPROM
ASCII
instruction
instruction
instruction
length
Functional description
for example
The drive ID address is 0x08
Read drive product information command

GID
0x01	1
2
Read the drive product number.
Return data: 32-bit unsigned number.
Issued: [0x08][0x01]
Returns: [0x08][0x01][0x12345678]

GVER
 0x02	2
2
Read the software version.
Magnification 100 times, V1.24 → 124
Return data: 16-bit signed number.
Issued: [0x08][0x02]
Returns: [0x08][0x02][0x007C]

Motor encoder related configuration
KN
0x10	16
4
Set the speed constant (K).
Set the motor speed constant in rpm/V
(turns per minute / volt).
Data: 16-bit signed number.
Issued: [0x08][0x10][0x007C]

GKN
0x11	17
2
Read the speed constant.
Return data: 16-bit signed number.
Issued: [0x08][0x11]
Returns: [0x08][0x11][ 0x007C]

R
0x12	18
4
Set the internal resistance of the motor.
Set the motor's terminal resistance in mΩ (millimeters
Europe).
Data: 16-bit signed number.
Issued: [0x08][0x12][0x0080]

GR
0x13	19
2
Read the internal resistance of the motor.
Return data: 16-bit signed number.
Issued: [0x08][0x13]
Returns: [0x08][0x13][ 0x0080]

N
0x14	20
4
Set the gear ratio.
Unit: 0.1, ie 128 means the gear ratio is
12.8.
Data: 16-bit signed number.
Issued: [0x08][0x14][0x0080]

GN
0x15	21
2
Read the gear ratio.
Return data: 16-bit signed number.
Issued: [0x08][0x15]
Returns: [0x08][0x15][ 0x0080]

SSP
0x16	22
6
Set the maximum allowable speed of the motor, suitable for
Any working mode.
Data: 32-bit signed number.
Issued: [0x08][0x16][0x12345678]

GSP
0x17	23
2
The maximum speed is allowed to read the set motor.
Return data: 32-bit signed number.
Issued: [0x08][0x17]
Returns: [0x08][0x17][ 0x12345678]

SMV
0x18	24
4
When the set speed is less than the minimum speed, the motor
Will brake.
Data: 16-bit signed number.
Issued: [0x08][0x18][0x000A]

GMV	25
0x19
2
Read the set minimum speed value.
Return data: 16-bit signed number.
Issued: [0x08][0x19]
Returns: [0x08][0x19][0x000A]

SPC
0x1A	26
4
Set the peak current of the motor.
Value range: 0~20000 mA
Data: 16-bit unsigned number.
Issued: [0x08][0x1A][0x2468]

GPC
0x1B	27
2
Read the set peak current.
Return data: 16-bit unsigned number.
Issued: [0x08][0x1B]
Returns: [0x08][0x1B][0x2468]
SCC
0x1C
4
Set the continuous current value of the motor
Value range: 0~10000 mA
Data: 16-bit unsigned number.
Issued: [0x08][0x1C][0x1234]

GCC
0x1D
2
Read the set continuous current value.
Return data: 16-bit unsigned number.
Issued: [0x08][0x1D]
Returns: [0x08][0x1D][ 0x1234]

ENC
0x1E	30
6
Set the encoder resolution, the parameter is the encoder 4 times the actual number of lines.
Data: 32-bit signed number.
Issued: [0x08][0x1E][0x000007D0]

GENC
0x1F	31
2
Read the encoder resolution.
Return data: 32-bit signed number.
Issued: [0x08][0x1F]
Returns: [0x08][0x1F][0x000007D0]

Drive operating mode and node address setting
SADR
0x28	40
4
Set the drive ID address
Value range: 2~127
Data: 16-bit signed number.
Issued: [0x08][0x28][0x0080]

GADR
0x29	41
2
Read drive ID address
Return data: 16-bit signed number.
Issued: [0x08][0x29]
Returns: [0x08][0x29][0x0080]

SMOD
0x2A	42
4
Set the current working mode:
1) Control mode (Bit2, bit1, bit0)
000: The speed controller is in effect;
001: The position controller is in effect;
010: The step controller is valid;
011: Torque control mode
Other: reserved
2) Channel selection (Bit5, bit4, bit3)
000: instruction protocol mode;
001: analog signal control;
010: PWM signal control;
011: pulse, direction control;
Other: reserved
3) Command protocol channel selection
(Bit8, bit7, bit6)
000: RS232 communication;
001: RS485 communication;
010: CAN communication;
Other: reserved
4) Enable hardware location range limit (Bit9)
0: Disable location range restrictions
1: Enable location range restrictions
5) Enable software location range limit (Bit10)
0: Disable location range restrictions
1: Enable location range restrictions
6) Simulated control mode to set motor steering
(Bit11)
0: The positive voltage is input and the motor rotates counterclockwise.
1: Enter a positive voltage and the motor rotates clockwise.
7) bit12, bit13, bit14, bit15: reserved.
Data: 16-bit unsigned number.
Issued: [0x08][0x2A][0x0400]

GMOD
0x2B	43
2
Read the current working mode.
Return data: 16-bit unsigned number.
Issued: [0x08][0x2B]
Returns: [0x08][0x2B][0x0400]
Driver working mode setting parameters

BAUD
0x30	48
6
Set the communication rate (unit: bps)
Data: 32-bit signed number.
Issued: [0x08][0x30][0x000F4240]

SMAV
0x31
4
Set the deadband voltage when the input voltage is absolute
When the value is less than the set value, the motor will brake.
Value range: 0 to 1000.
Unit: mV
Data: 16-bit signed number.
Issued: [0x08][0x31][0x0080]

GMAV
0x32
2
Read the set deadband voltage value.
Return data: 16-bit signed number.
Issued: [0x08][0x32]
Returns: [0x08][0x32][0x0080]

SPH
0x33	51
6
Set the upper limit of the position range.
Set the positive maximum position of the motor motion
Surrounding, the value range: 0 ~ 2100000000
Data: 32-bit signed number.
Issued: [0x08][0x33] [0x12345678]

GPH
0x34	52
2
Read the upper limit of the position.
Return data: 32-bit signed number.
Issued: [0x08][0x34]
Returns: [0x08][0x34] [0x12345678]

SPL
0x35	53
6
Set the lower limit of the position range.
Issued: [0x08][0x35] [0xF2345678]
Set the reverse maximum position of the motor motion
Surrounding, the value range: 0 ~ -2100000000.
Data: 32-bit signed number.

GPL
0x36	54
2
Read the lower limit of the position.
Return data: 32-bit signed number.
Issued: [0x08][0x36]
Returns: [0x08][0x34] [0xF2345678]

STW
0x37
4
Set the step width.
Set the step taken for each pulse motor input
number.
Data: 16-bit signed number.
Released: [0x08][0x37][0x0005]

GTW
0x38
2
Read the step width.
Return data: 16-bit signed number.
Issued: [0x08][0x38]
Returns: [0x08][0x38][0x0005]

SER
0x39
4
Set the maximum position tracking error of the step mode.
SER255, indicating that the position tracking error range is
-255~+255; unit: encoder resolution.
Data: 16-bit signed number.
Issued: [0x08][0x39][0x00FF]

GER
0x3A
2
Read step mode maximum position tracking error.
Return data: 16-bit signed number.
Issued: [0x08][0x3A]
Returns: [0x08][0x3A][0x00FF]

SDEV
0x3B
4
Set the speed deviation range.
Set the allowable between the actual motor and the preset speed
The range of deviation.
Data: 16-bit signed number.
Issued: [0x08][0x3B][0x0080]

GDEV
0x3C
2
Read the speed deviation range.
Return data: 16-bit signed number.
Issued: [0x08][0x3C]
Returns: [0x08][0x3C][0x0080]

SDCE
0x3D
4
The delay indicates a fault.
Set the delay to indicate the overload fault time, the unit
In milliseconds.
Data: 16-bit signed number.
Issued: [0x08][0x3D][0x0800]

GDCE
0x3E
2
Read the set fault delay indication time.
Return data: 16-bit signed number.
Issued: [0x08][0x3E]
Returns: [0x08][0x3E][0x0800]

PID debug setting instruction
A
0x58	88
4
Set acceleration
Issued: [0x08][0x58][0x0080]
Set a new acceleration value; value range:
1 to 30000.
Data: 16-bit signed number.

GA
0x59	89
2
Read the set motor acceleration value. Numerical range
Wai: 1 ~ 30000.
Return data: 16-bit signed number.
Issued: [0x08][0x59]
Returns: [0x08][0x59][0x0080]

AP
0X5A	90
4
Set the current loop scaling factor.
Data: 16-bit signed number.
Issued: [0x08][0x5A][0x0080]

GAP
0x5B	91
2
Read the current loop scaling factor.
Return data: 16-bit signed number.
Issued: [0x08][0x5B]
Returns: [0x08][0x5B][0x0080]

AI
0x5C	92
4
Set the current loop integral factor.
Data: 16-bit signed number.
Issued: [0x08][0x5C][0x0040]

GAI
0x5D	93
2
Read the current loop integral coefficient.
Return data: 16-bit signed number.
Issued: [0x08][0x5D]
Returns: [0x08][0x5D][0x0040]

AD
0x5E	94
4
Set the current loop differential coefficient.
Data: 16-bit signed number.
Issued: [0x08][0x5E][0x0000]

GAD
0x5F	95
2
Read the current loop differential coefficient.
Return data: 16-bit signed number.
Issued: [0x08][0x5F]
Returns: [0x08][0x5F][0x0000]

P	96
0x60
4
Set the speed loop scaling factor.
Data: 16-bit signed number.
Issued: [0x08][0x60][0x0080]

GP	97
0x61
2
Read the speed loop scaling factor.
Return data: 16-bit signed number.
Issued: [0x08][0x61]
Returns: [0x08][0x61][0x0080]

I	98
0x62
4
Set the speed loop integral factor.
Data: 16-bit signed number.
Issued: [0x08][0x62][0x0040]

GI
0x63	99
2
Read the speed loop integral coefficient.
Return data: 16-bit signed number.
Issued: [0x08][0x63]
Returns: [0x08][0x63][0x0040]

D
0x64	100
4
Set the speed loop differential coefficient.
Data: 16-bit signed number.
Issued: [0x08][0x64][0x0000]

GD
0x65	101
2
Read the speed loop differential coefficient.
Issued: [0x08][0x65]
Return data: 16-bit signed number.
Returns: [0x08][0x65][0x0000]

MP
0x66	102
4
Set the position loop scale factor.
Data: 16-bit signed number.
Issued: [0x08][0x66][0x0080]

GMP
0x67
2
Read the position loop scale factor.
Return data: 16-bit signed number.
Issued: [0x08][0x67]
Returns: [0x08][0x67][0x0080]

MK
0x68
4
Set the position loop speed feed forward coefficient.
Data: 16-bit signed number.
Issued: [0x08][0x68][0x0040]

GMK
0x69
2
Read the position loop speed feed forward coefficient.
Return data: 16-bit signed number.
Issued: [0x08][0x69]
Returns: [0x08][0x69][0x0040]
Set boot to find zero command

SPOF
0x75
4
Set the look for the zero mark.
1: Boot to find the zero position
0: boot does not look for zero
Data: 16-bit unsigned number.
Issued: [0x08][0x75][0x0001]

GPOF
0x76
2
Read to find the zero mark.
1: Boot to find the zero position
0: boot does not look for zero
Return data: 16-bit unsigned number.
Issued: [0x08][0x76]
Returns: [0x08][0x76][0x0001]

SOV
0x77
6
Set to find the zero speed.
Data: 32-bit signed number.
Issued: [0x08][0x77][0x00001234]

GOV
0x78
2
Read to find the zero speed.
Return data: 32-bit signed number.
Issued: [0x08][0x78]
Returns: [0x08][0x78][0x00001234]

SOP
0x79
6
Set to find the maximum range of zeros.
Data: 32-bit signed number.
Issued: [0x08][0x79][0x12345678]

GOP
0x7A
2
Read to find the maximum range of zeros.
Return data: 32-bit signed number.
Issued: [0x08][0x7A]
Returns: [0x08][0x7A] [0x12345678]

5. Drive control instructions for controlling drive operation
ASCII
instruction
instruction
Functional description
for example
instruction
length
The drive ID address is 0x08

Drive system operation instruction

ENA
0x80	128
2
Enable control.
The drive loads the motor.
Issued: [0x08][0x80]

DIS
0x81	129
2
Offline control.
The drive releases the motor and the motor rotates inertially.
Issued: [0x08][0x81]

ESA
0x82	130
2
Save Settings.
Save basic parameters and control mode parameters to EEPROM.
Issued: [0x08][0x82]

FCFG
0x83	131
2
reset.
Reset all parameters to the default settings at the factory
Set.
Issued: [0x08][0x83]

SBS
0x84	132
2
Emergency stop command (this command is strictly prohibited to use frequently,
Free of damage to the drive and motor)
Applying the command driver in any mode will
Brake the motor immediately (not subject to acceleration),
The drive enters an emergency stop state;
Issued: [0x08][0x84]

CBS
0x85	133
2
Cancel emergency stop control.
The drive restores the originally set operating mode.
Issued: [0x08][0x85]
Speed ​​control command

V
0x90	144
6
Set the running speed.
The motor starts moving at the set speed.
Data: 32-bit signed number.
Issued: [0x08][0x90][0x00123456]

GV
0x91	145
2
Read the actual speed.
Return data: 32-bit signed number.
Issued: [0x08][0x91]
Returns: [0x08][0x91][0x00123456]

GVE
0x92	146
6
Read speed error.
Return data: 32-bit signed number.
Issued: [0x08][0x92]
Returns: [0x08][0x92][0x00000012]

GSV
0x93
6
Read the speed of the settings.
Return data: 32-bit signed number.
Issued: [0x08][0x93]
Returns: [0x08][0x93][0x00123456]
Position control instruction

PO
0x98	152
6
Set the absolute position.
Set the current position of the motor to the absolute position.
It can only be set when the motor is stopped.
Data: 32-bit signed number.
Issued: [0x08][0x98][0x00000000]

M
0x99	153
6
Set the absolute position and start the position movement.
The motor starts moving to the set position.
Data: 32-bit signed number.
Issued: [0x08][0x99][0x12345678]

MR
0x9A	154
6
Set the relative position and start the position movement.
The motor begins to move to the set relative position.
Data: 32-bit signed number.
Released: [0x08][0x9A][0x00001234]

GM
0x9B	155
6
Read the actual location.
Return data: 32-bit signed number.
Issued: [0x08][0x9B]
Returns: [0x08][0x9B][0x12345678]

GME
0x9C	156
6
Read position tracking error (also including stepping mode)
formula).
Return data: 32-bit signed number.
Issued: [0x08][0x9C]
Returns: [0x08][0x9C][0x00000012]

GSM
0x9D	157
6
Read the location of the settings.
Return data: 32-bit signed number.
Issued: [0x08][0x9D]
Returns: [0x08][0x9D][0x12345678]

MM
0x9E	158
6
Set the absolute position but not start the position
move. Data: 32-bit signed number.
Issued: [0x08][0x9E][0x12345678]

MMR
0x9F	159
6
Set relative position but does not start position
move. Data: 32-bit signed number.
Released: [0x08][0x9F][0x00001234]

MRUN
0xA0	160
2
Starting position movement
Issued: [0x08][0xA0]

6. Condition monitoring instruction
ASCII
instruction
instruction
instruction
length
Functional description
Example (Device
for example

GC
0xD0	208
2
Read the actual current consumption value.
Return data: 16-bit signed number.
Issued: [0x08][0xD0]
Returns: [0x08][0xD1][0x0080]

GT
0xD1	209
2
Reading temperature
Read the drive case temperature (°C).
The temperature is a 16-bit signed number.
Unit: Celsius
Return data: 16-bit signed number.
Issued: [0x08][0xD1]
Returns: [0x08][0xD1][0x0020]

GSI
0xD2	210
2
Read system information
Return data: 16-bit unsigned number.
Read system status values, bit numbers from left to right:
1) Motor controlled (bit0)
1: The motor is controlled;
0: The motor is not controlled;
2) Motor steering (bit1)
1: the motor rotates clockwise;
0: The motor rotates counterclockwise;
3) Emergency stop status (bit2)
1: The motor stops suddenly;
0: The motor is normal;
4) Left limit status (bit3)
0: normal state
1: Left limit status
5) Right limit status (bit4)
0: normal state
1: Right limit state
6) Position status (bit5)
0: The specified location has not arrived;
1: The specified location has arrived;
7) Speed ​​status (bit6)
Issued: [0x08][0xD2]
Returns: [0x08][0xD2][0x0080]
0: The specified speed has not arrived;
1: The specified speed has arrived;
8) Boot to find the zero mark (bit7)
0: Zero is not found;
1: Zero has been found;

9) System numerical unit system flag (bit8)
0: Class A system numerical unit system.
1: Class B system numerical unit system.
Specific A, B system numerical unit
See the description below for details.
10) Other: Reserved
GFI
0xD3
2
Read fault information (by bit0-bit15
16-digit number, 0: no fault, 1:
Indicates a fault).
Return data: 16-bit unsigned number.
The digits represent from left to right:
Bit0: Overheat alarm
Bit1: Overheat protection
Bit2: Overcurrent protection
Bit3: Undervoltage protection
Bit4: Overvoltage protection
Bit5: Speed ​​out of control protection
Bit6: Reserved
Bit7: Overload protection
Bit8: Position tracking error overrun protection
Bit9: EEPROM error protection
Bit10-Bit15: Reserved
Issued: [0x08][0xD3]
Returns: [0x08][0xD3][0x0000]

GEI
0xD4	212
2
System error message.
Issued : [0x08][ 0xD4 ]
Return data: 16-bit unsigned number.
The specific category is pending.
Returns: [0x08][ 0xD4 ][0x0000]
7. A, B type system numerical unit description
The A/B type system numerical unit system is set by the 8th bit of the DIP switch, S8 is ON for the Class A system numerical unit system, and S8 is OFF for
Class B system numerical unit system. The factory default is the Class A system numerical unit system.
Class A system numerical unit system: speed and speed error in revolutions per minute (RPM), acceleration in revolutions per second 2 (R/S 2 ), bits
The position error is set in units of encoder resolution, and the step width (STW) unit in step pulse mode is also an encoder resolution.
Class B system numerical unit system: speed and speed error in units of 0.01 degrees/second, acceleration in degrees/second 2 , position and position
The error is in units of 0.01 degrees, and the step width (STW) unit in step pulse mode is also 0.01 degrees.

Page 21

In order to make the drive work better, the parameters must be set according to the actual situation before application. The parameter settings can be divided into the following categories:
(1) Motor encoder related parameter settings
1) Set the maximum speed allowed by the motor:
The DC servo motor has a rated speed at the rated working voltage. According to the actual needs, the maximum speed allowed by the motor should be
Less than the rated motor speed, generally can be set to less than 80% of the rated motor speed. Note: This parameter must be set.
2) Set the motor to allow the lowest speed:
In the actual work, in order to make the control motor run more smoothly, the minimum speed can be set. When the motor running speed is required to be less than this value, the motor is required.
It will stop running. In addition, this parameter must be set to achieve absolute stop during analog speed control or PWM speed control. silent
The setting is 0.
3) Set the peak current of the motor:
In order to make the motor have better transient overload performance during acceleration and deceleration, the peak current can be set, but the current should be less than the stall current of the motor.
Note: The peak current value of the motor should not exceed the peak current value allowed by the drive.
4) Set the continuous current value of the motor:
In order to make the motor and the driver work stably and reliably for a long time, the continuous working current of the motor can be set, and the motor can work under continuous current without
It will be too hot. Generally, the continuous current value should be half of the peak current and current.
Note: The continuous current value of the motor should not exceed the continuous current value allowed by the drive.
5) Set the encoder resolution:
This drive can only be configured with incremental photoelectric encoders. The general encoder will nominally number of lines, such as 500 lines. This drive will encode
The output signal of the device is processed by 4 times, so the encoder resolution is set to 4 times the actual number of lines, that is, the 500 line encoder.
The resolution is 2000. Note: This parameter must be set.
6) Set the gear ratio (also called electronic gear):
This ratio should be set when the motor is equipped with a gear unit.
7) Set the motor speed constant: This parameter can be set in this drive.
8) Set the internal resistance of the motor: This parameter can be set in this drive.

Page 22

1. Initialization settings
The default parameters when the drive is shipped from the factory are as follows:
Instruction parameter
Description
Instruction parameter
Description
ENA
Internal enable
SPH2000000000
Set the upper limit of the location range
SMOD
Operating mode
Speed ​​control mode
The signal source is CAN2.0
SPL-2000000000
Set the lower limit of the position range
BAUD500000
CAN communication baud rate
500000bps
MP100
Position scale factor 100
SADR127
Node address 127
MK50
Speed ​​feed forward coefficient 50
ENC2000
Encoder resolution 2000
(500 lines)
P50
Speed ​​proportional coefficient 50
SMV0
Minimum speed 0RPM
I30
Speed ​​integral coefficient 30
N1
Transmission ratio 1
D0
Speed ​​differential coefficient
SPOF0
Booting does not look for zero
SPC20000
Maximum peak current 20A
SMAV0
Dead zone voltage 0mV
SCC10000
Maximum continuous current 10A
SDCE3000
Overload protection delay time
3000ms
Class A parameter (unit RPM)
Class B parameters (unit: 0.01°/S)
SSP5000
Maximum speed 5000RPM
SSP360000
Maximum speed 360°/S
SOV60
Zero speed 60
SOV36000
Zero speed 36 ° / S
SOP1000
Zero finding range 1000
SOP18000
Zero finding range 18000
STW1
Step width 1
STW18
Step width 18
SER2000
Step mode maximum tracking error
SER36000
Step mode maximum tracking error
difference
A50
Acceleration 50R/S 2
A3600
Acceleration 3600°/S 2
Note: The above parameters are the factory default values, and the user needs to reset and store according to the selected motor, encoder and load conditions.
2. CAN2.0B speed control mode
(1) Signal source: CAN2.0B communication
(2) Setting mode: CAN speed control mode
(3) Common instructions:
• Set speed: V + parameters
Such as: V1000: Start the quick control mode, the motor starts to move at the set speed.
• Set acceleration: A + parameter
Such as: A100 , set the acceleration value, the unit is the revolution every second square (R / S 2 ) , the range: 1 to 30000.
4. CAN2.0B position control mode
(1) Signal source: CAN2.0B communication
(2) Setting mode: CAN2.0B position control mode
(3) Common instructions:
• Set absolute position: PO + parameter
Set the current position to the absolute position corresponding to the parameter.
For example: PO0, the current position is set to absolute zero.
• Set maximum speed: SSP + parameters
• Set maximum acceleration: A + parameter
• Set the target position with absolute position parameters: M + parameters
Such as: M2000, moving from the current position to the absolute position 2000.
• relative position of the target position parameter settings: MR + parameters
Such as: MR2000, moving 2,000 units in the forward direction from the current position.

six. Fault protection and reset
1. Security Level
The protection mechanism is divided into three levels of security: alarm, auto-recovery, and status latching. The protection mechanism of fault information at each level is as follows:
• Alarm: The drive continues to work, the flag is set, and the FAULT signal is output;
• 自动恢复：故障发生后，系统关断PWM，标志置位， FAULT 信号输出；
故障消失后，自动恢复到工作状态，标志清除， FAULT 信号停止输出；
• 状态锁存：故障发生后，系统关断PWM，标志置位， FAULT 信号输出；
故障标志只能通过发送ENA 指令或外部EN 信号置高清除。
2．故障保护依据
（1）过流保护
硬件过流保护：当瞬间电流大于 13A ，硬件自动保护，关断PWM输出，此保护并不影响故
障状态信息位 ；当电流小于 13A ，硬件保护关闭，使能 PWM 输出；
软件过流保护：当电流持续大于 峰值电流的时间超过过流延迟保护时间，将产生保护。
（4）过压、欠压保护
当电源电压低于10.5V 时系统将启动欠压保护；
当电源电压高于54 伏时系统将启动过压保护；
（5）速度失控保护
驱动器无法控制电机按照设定的指令运行，将产生保护。
（6）过载保护
当电流持续大于连续电流的时间超过过载保护延迟时间，将产生过载保护。
（7） EEPROM 出错保护
如果EEPROM 读取的数据信息不正确，驱动器保护，电机停止运转。
3. 故障信息读取
故障读取指令：GFI，驱动器返回信息如下 （以bit0-bit15,16 位数字表示，0：表示无故障，1：表示
有故障） ：
保护类别
标志位
安全级别
关断PWM 输出
FAULT 输出
过流保护
Bit2
状态锁存
Yes
Yes
欠压保护
Bit3
自动恢复
Yes
Yes

Page 25

西安铭朗电子科技有限责任公司
·MLDS3605C User Manual·
Company Address: Room 1103, Block H, Wangzuo Modern City, Tangyan Road, High-tech Zone, Xi'an (PR: 710075)
Tel: 86-29-88892291 15802975566 Fax: 86-29-88892265
Website: http://www.mosvo.com
The first 24- page Total 29 Ye
Overvoltage protection
Bit4
Automatic recovery
Yes
Yes
Out of control
Bit5
Status latch
Yes
Yes
Overload protection
Bit7
Status latch
Yes
Yes
EEPROM error
protection
Bit9
Status latch
Yes
Yes
Note: Once the state is latched, the driver will turn off the PWM output and can only be cleared by sending an ENA instruction or an external EN signal.
When the ENA signal is active or the EN signal is high, if the fault disappears, the corresponding fault flag is automatically cleared.

Page 26

Xi'an Minglang Electronic Technology Co., Ltd.
·MLDS3605C User Manual·
Company Address: Room 1103, Block H, Wangzuo Modern City, Tangyan Road, High-tech Zone, Xi'an (PR: 710075)
Tel: 86-29-88892291 15802975566 Fax: 86-29-88892265
Website: http://www.mosvo.com
The first 25 Total 29 Ye
Seven. Parameter setting and PID debugging
1. parameter settings
(1) Connect the CAN communication port and set it on the Servo Operation Management System. For details, please refer to the software instructions.
(2) The user sets it according to the software protocol.
2. Parameter saving
(1) Use the "Servo Control System" to save, see the software manual for details;
(2) The user saves using the ESA instruction.
Note: The parameters downloaded during the debugging process will not be saved if they are saved by the ESA instruction.
3. PID debugging
The customer needs to debug the PID parameters according to his actual application, and can intuitively observe the debugging on the Servo Operation Management Software.
effect. The PID parameters are generally different depending on the motor and load. Adjusting the PID parameters can improve the dynamics of the system. Speed ​​control
System mode (CAN2.0B/PWM signal source), position control mode (CAN2.0B signal source), step control mode generally need different
PID value, the customer needs to adjust the parameters according to their actual application. According to the actual application needs of customers, the following situations are classified:
(1) Only the speed control mode is applied, and the PID debugging method is as follows:
• Set the maximum speed (ie rated speed).
For example: -> SSP5000;
• Set the acceleration.
For example: -> A100;
• Increase the P-factor and I-factor at the same time, the D-factor is 0, and keep the P-factor as a factor of 3 to 0.2 times the I-factor.
Example: -> P20
-> I10
-> D0
• Increase the speed from zero to the rated speed, then decrease to zero, and observe the speed response curve, speed stability, and overshoot.
• Repeat the above two steps (including adjusting the multiple of P and I) until the best performance;
• To speed up the adjustment process, adjust the D factor appropriately to make the system perform better. ;
(2) CAN2.0B position control mode, PID debugging method is as follows:
• Set the maximum speed. For example: -> SSP5000;
• Set the acceleration.
For example: -> A100;
• Increase both P and I, D is 0, keeping P a factor of 3 to 0.2 for I.

Page 27

Xi'an Minglang Electronic Technology Co., Ltd.
·MLDS3605C User Manual·
Company Address: Room 1103, Block H, Wangzuo Modern City, Tangyan Road, High-tech Zone, Xi'an (PR: 710075)
Tel: 86-29-88892291 15802975566 Fax: 86-29-88892265
Website: http://www.mosvo.com
The first 26 Total 29 Ye
E.g:
-> P20
-> I10
-> D0
• Move the position from 0 to 100000 and then decrease to 0 to observe the position response curve, overshoot, and speed stability.
E.g:
->PO
->M100000
->GSI
Waiting for arrival location
->M0
->GSI
Waiting for arrival location
• Repeat the above two steps (including adjusting the multiple of P and I) until the best performance;
• To speed up the adjustment process, adjust the D factor appropriately to make the system perform better.
4. Operational condition monitoring
After the user successfully modifies the parameters, the effect of the motion control can be monitored in real time on the Servo Operation Management System software to facilitate adjustment.
parameter.

Page 28

Xi'an Minglang Electronic Technology Co., Ltd.
·MLDS3605C User Manual·
Company Address: Room 1103, Block H, Wangzuo Modern City, Tangyan Road, High-tech Zone, Xi'an (PR: 710075)
Tel: 86-29-88892291 15802975566 Fax: 86-29-88892265
Website: http://www.mosvo.com
The first 27 Total 29 Ye
Eight. Application examples
1. Initialization settings
Step 1: Connect the motor, encoder, and power supply to the drive properly and turn on the power.
Step 2: Open the Servo Control Management System and connect the drive.
Step 3: Make the following settings based on DC motor and encoder parameters:
SPC8000
Maximum peak current 8A
SCC4500
Maximum continuous current 4.5A
A50
Acceleration 50
P50
Scale factor 50
I120
Integral coefficient 120
D0
Differential coefficient 0
SSP8000
The maximum speed is 8000RPM, please modify this value according to the rated motor speed.
ENC2000
Encoder resolution 2000 (500 lines), please modify this value according to the actual encoder resolution
Step 4: Store the parameters.
2. CAN2.0B speed control
Step 1: After the initial setup is complete, make the following settings:
DIS
Drive release motor
SMOD128
Switch to speed control mode, CAN source
ENA
Internal enable is valid, motor is loaded
V1000
Control the motor to run at 100RPM
Step 2: Perform PID debugging to get the best speed control performance
Step 3: Save the parameters
ESA
Save the configuration to the built-in EEPROM of the drive
Step 4: Turn off the power, re-power, and use the RS232 command to control motor operation.
4. CAN2.0B position control
Step 1: After the initial setup is complete, make the following settings:
DIS
Drive release motor

Page 29

Xi'an Minglang Electronic Technology Co., Ltd.
·MLDS3605C User Manual·
Company Address: Room 1103, Block H, Wangzuo Modern City, Tangyan Road, High-tech Zone, Xi'an (PR: 710075)
Tel: 86-29-88892291 15802975566 Fax: 86-29-88892265
Website: http://www.mosvo.com
The first 28 Total 29 Ye
SMOD129
Switch to position control mode, CAN source
ENA
Internal enable is valid, motor is loaded
PO0
Clear position
M200000
Set the relative position 200000 to perform position control
Step 2: Perform PID debugging to get the best bit control performance
Step 3: Save the parameters
ESA
Save the configuration to the built-in EEPROM of the drive
Step 4: Turn off the power, reapply, and use CAN2.0B to control motor operation.

Page 30

Xi'an Minglang Electronic Technology Co., Ltd.
·MLDS3605C User Manual·
Company Address: Room 1103, Block H, Wangzuo Modern City, Tangyan Road, High-tech Zone, Xi'an (PR: 710075)
Tel: 86-29-88892291 15802975566 Fax: 86-29-88892265
Website: http://www.mosvo.com
The first 29 Total 29 Ye
nine. common problem
1. Relationship between ENA/DIS instruction and external enable signal EN
The external enable signal EN has the highest priority. When it is low, the ENA/DIS instruction operation is invalid. When it is high, ENA
The /DIS instruction operation is valid;
2. About SBS Emergency Stop Instructions
The SBS command can be used when the motor needs an emergency stop during operation. But this command will be produced for motors and drives at heavy loads and high speeds.
Certain injuries are caused, and it is strictly forbidden to use them frequently; to cancel the emergency stop state, you can use the CBS command or re-energize the drive.
.3 on the ESA Directive
When using the ESA instruction to store parameters, the motor should be stopped, otherwise a short-term imbalance will occur;